VT10 PIN CONFIGURATION (WIRING DIAGRAM)

| PIN NO | Definition | Corresponding Cable color | Description/Specification |
| --- | --- | --- | --- |
| 1 | Power | RED | DC 0~30V |
| 2 | Ground | BLACK |  |
| 3 | Input1 | WHITE | Positive triggered (above 5V as the trigger condition) ** Used for power sleeping mode activation/deactivation |
| 4 | Input2 | GRAY | Positive triggered (above 5V as the trigger condition) |
| 5 | Input 3 | GREEN | Negative triggered (below 0.8V) |
| 6 | Input 4 | PURPLE | Negative triggered (below 0.8V) |
| 7 | Output 1 | YELLOW | Negative triggered ( Io=160mA, Ipeak: 320mA) |
| 8 | Output2 | ORANGE | Negative triggered ( Io=160mA, Ipeak: 320mA) |
| 9 | Output3 | BROWN | Negative triggered ( Io=160mA, Ipeak: 320mA) |
| 10 | Output4 | BLUE | Negative triggered ( Io=160mA, Ipeak: 320mA) |