BODY CAMERA             USER’S MANUAL

Table of Content

Preface	3

Brief introduction and main features	4

Buttons Descroption	5

Operations	7

Specification	11

Packing List	12

Preface

Thank you for using our Body Cameras. This manual is applicable for BC001 series Body Cameras. Please read the manual carefully before using the devices. Please keep this manual for reference in the future. The content of this manual is subject to be changed without notice.

Important notice

Please keep ventilation for the device to prevent overheating.

When smoke or smell or noise comes out from the device, shut down the power and remove the power cable immediately, and then contact your supplier in time.

Please contact your supplier if the device is not working properly. Please do NOT disassemble or modify the device in any way.

Please do NOT charge the device at high temperature over 45 degrees Celsius, or else it could cause the explosion of the battery.

Please read this manual carefully before using the device and follow the instruction in this manual when using the device.

Please do NOT use the device under the circumstance: over humidity or high temperature, avoid using the device around the place: strong signal interference source and shielding-barrier equipment.

  Avoid putting the device under sunlight exposure and stuffy place(ignoring it could cause fire accident)

Please backup the data in the device timely.

Please keep the camera clean to get the best recording file and pictures.

Please keep your password and user name in safe place.

Brief introduction and main features

Brief introduction

The body cameras are the portable devices that can record video and audio. The devices can also transmit live video and audio through 3G or 4G, do live tracking with GPS. The devices have a TFT monitor and buttons on it and user can operate the device easily. The body cameras are usually used by police man, security guard, and other law enforcement officers.

Main features

- The device is in compact size and suitable for portable use of recording.

- User can get live video and audio through 3G, 4G or WiFi,

- User can get live tracking of the device through built-in GPS in the device. The GPS data will also be recorded into the record file with audio and video, so user can get the location in the record file.

- Use lithium battery for power supply. Device can be recording continuously for 12 hours with 2 batteries.

- Built-in 16G storage space. (32G~128G optional storage space）

- Built-in 40 million pixel cameras, support recording at 1080P, 720P or D1 resolution, support taking picture with 40 million pixels, 32 million pixels and 2 million pixels.

- Support IR. Support recording at night.

- Record file name have information on date, time, record type, which make it easier for searching and document.

- User can explore, search and playback the files on the device.

- Support panic button. The panic button alarm can be sent to control center through 3G/4G.

- Device can display device ID, user ID, date and time.

- Device can display information about battery usage, charging status, system time and memory space. Device has light indication for power on, recording video or audio. Green light indicates power on, red light indicates video recording, yellow light indicates audio recording.

- Device can report event alarm, including alarm for battery running low, insufficient memory space alarm etc.

- Device has log files. Device with log events including power on/off, recording video, recording audio, taking pictures, GPS status fixed, 3G/4g connection, and WiFi connection.

Buttons Description

Buttons Description

| Buttons | Icon | Action | Function |
| --- | --- | --- | --- |
| Power |  | Short press | When device is ON, turn on/off the monitor. When device is OFF, power on device. |
|  |  | Long Press | Power off device |
| Talk Back | PTT | Long press | Start talking back. |
| Record / Panic |  | Short Press | When device is ON, short press will start recording video, short press again will stop recording and save video files. When device is OFF, short press will power on the device. |
|  |  | Long Press | Long press for over 3 seconds will start a panic alarm and this alarm can be sent through 3G/4G to server. |
| Snap |  | Short Press | When device is ON, short press can make the device to take one picture and save the picture. |
|  |  | Long Press | Long press will turn on the flash light. |
| Audio Recording |  | Short Press | When device is idle, short press will start recording audio, press again will stop recording and save the audio. |
| Laser |  | Short Press | When device is idle, short press will turn on the laser light. The laser light is used for locating the direction of the camera. |
|  |  | Long Press | When device is idle, long press will turn on the IR for recording at night. |
| Multifunctional interface |  | Connect | For connecting with earphone, mic etc. |
| SIM | SIM | Insert | Insert SIM card for 3G/4G connection |
| USB | USB | Connect | Data transmitting, Charging |
| Menu/OK |  | Short Press | Short press to display the main menu in the monitor. Short press to confirm what you have selected. |
| UP |  | Short Press | Scroll up the menu. |
| DOWN |  | Short Press | Scroll down the menu. |
| Return / Play |  | Short Press | 1. When menu is displayed, short press will return back to the upper level menu; 2. When device is idle, short press will show the play back menu and user can choose to play the video files, pictures, audio files. |

Device Indicator

| Color | Description |
| --- | --- |
| Green | Idle |
| Red | Recording Video |
| Yellow | Recording Audio |

Operations

- Power On/Off

Short press the “Power” button, the device will be turned on. When the device is ON, short press the “Power” button will turn On/Off the monitor, press and hold the “Power” button will turn off the device.

- Record Video

When the device is ON, short press the “Record” button to start recording, the device will vibrate once and the device indicator will turn red. When the device is recording, short press the “Record” button again will stop recording and start saving files, the device will vibrate once and beep.

When the device is OFF, press the “record” button to power on the device.

At night, user can long press the “Laser” button to turn on the IR. In the IR mode, the picture will be black and white.

- Record Audio

When the device is ON, press “Audio Record” button to start recording, the device will vibrate once and the device indicator will turn yellow. Press the “Audio Record” button again, the device will stop recording audio and save the audio file.

- Take Picture

When the device is ON, press “Snap” button to take pictures.

- IR

Press and hold the “IR” button, user can turn On/Off the IR light. When the IR is ON, the recording pictures will be black and white.

- Play Back

Short Press the “Play” button, the “Playback” menu will be displayed.

Use “UP” and “DOWN” button to choose the directory and file to play back.

6.1 Play back video files

In “Video” file directory, there are directories named with

date and hour, press “OK” button to open these directories

and choose the file and press “OK” button to play back.

The video file is in the format of AVI.

6.2 View the pictures

In the “Photo” directory, there are directories named with

date and time. Choose the picture file and press “OK”

button to view the pictures. The pictures is in JPG format.

6.3 Play Audio

In the “Audio” directory, there are directories named

with date and hour. Choose the audio file and press “OK”

to play the audio. The audio file is in the WAV format.

- Settings

Note: when the device is idle, press “menu” button to show the “Setting” menu. Press “OK” button to choose the sub-menu. Press “UP” and “Down” to scroll up and down in the menu. Press “OK” to choose the menu or value. Press “Return” to return to the upper level menu.

7.1 Record Resolution

The resolution for recording is 1080P (1920*1080). User can choose 1080P

7.2 Record FPS

The default record FPS is 30 frames per second (fps). User can choose from 5fps to 30fps.

7.3 Record Quality

The default recording quality is “High”. User can choose from “Super”, “High”, “Medium” and “Low”. The value of the bitrate is as following.

| Recording Quality | Super | High | Medium | Low |
| --- | --- | --- | --- | --- |
| bitrate | 8M | 6M | 4M | 3M |

7.4 Live Resolution

The Live resolution is the resolution for video transmission through 4G/3G. The default resolution is (1280*720), user can choose 1080P(1920*1080)/720P（1280*720）/VGA (640*480).

7.5 Live View FPS

The Live view FPS for video transmission through 4G/3G. The default is 30fps, user can choose from 5fps to 30fps.

7.6 Live Quality

The default value for live quality is “medium”. You can choose from “Super”, “High”, “Medium” and “Low”.

|  | Super | High | Medium | Low |
| --- | --- | --- | --- | --- |
| 1080P | 4 M | 3 M | 2 M | 1 M |
| 720P | 3 M | 2M | 1.5M | 800K |
| VGA | 1.5 M | 1M | 700K | 350K |

7.7 Live mode

The default mode is fluency first, which can give you a fluent live video, and the other is quality first that can give you a good quality of live video.

7.8 Picture Size

Set the resolution for taking pictures, the default value is “1920*1080”, User can choose from “1920*1080” to “8640*4752”.

7.9 USB Mode

The default USB mode is “Auto”. User can choose from “Auto”, “Host” or “Device” mode.

7.10 3G/4G

The 3G/4G mode is used to turn On/Off 3G/4G. The default mode is “On”.

7.11 LAN

This is used to turn On/Off the LAN port. This feature is

reserved for future use.

7.12 WIFI

Used for turn On/Off the WiFi. By default, the WiFi is off.

7.13 LCD Brightness

Used for controlling the monitor’s brightness. Given “High”, “Medium”, “Low” 3 options.

7.14 Auto Screen Off

The timeout value for turning off screen automatically. The default value is 30 seconds, user can choose from options “5 minutes”, “3 minutes”, “1 minute”, “30 seconds” and “off”.

7.15 Record Mode

The record mode can be “Auto” and “Manual”. When it is “Auto”, device will record video automatically and can NOT be stopped by pressing “Record” button.

7.16 IR Switch

The IR switch mode can be “Auto” and “Manual”. “Auto” means device can turn on IR automatically when the surrounding’s brightness is turning low, and the IR will shift back when the brightness comes back.

7.17 MIC Volume

The microphone volume can be from 0 to 10. The default value is 8.

7.17 SPK Volume

The speaker volume can be from 0 to 10. The default volume is 9.

7.18 Voice reminder

Turn On/Off the audio when pressing buttons. Is NOT including the beep reminder.

7.19 External Audio

The options include “Headphone”, “Interphone”, “None”.

7.20 File Length

File length means the length of the saved video for recording.

You can select from 5 mins to 30 mins.

7.21 Pre-Recording

Pre-Recording means that device records the video in advance when you press the “record” button. The options include 5s, 10s, 20s, off.

7.22 Post-Recording

Post-Recording means that device will remain recording within the setting time after you press the “record” button to end the record. The options include 5s, 10s, 20s, off.

7.23 Laser

The default is “disable”, which means that you can NOT turn on laser light by pressing “IR/Laser” button, and you can change the setting to “enable” to make it happen.

7.24 Language

Set the language for the device. According to the bodycamera’s registration, the default is English.

7.25 Setting Mode

The default is “off”, when it goes to “on”, accessing to bodycamera’s

memory card will be stopped.

7.26 Device Information

The device information includes hardware version, firmware version, MCU version, Device SN, vendor ID, product ID, Lan IP, 3G/LTE IP、wifi IP, Gate way, DNS0, DNS1, Server IP, Server Port, 4G/3G Module, IMEI, Operator Name, Signal Level, Wifi Module, Wifi MAC, AP Name.

Specification

| 1 | LCD | 320x240, 2.0 inch TFT-LCD High-Resolution Color Display |
| --- | --- | --- |
| 2 | Compatible OS | Windows7/Windows8/Windows10 |
| 3 | Image Angle | HOV ≥130° |
| 4 | Photo Format | JPEG |
| 5 | Night Vision | Up to 8 Meters with Visible face image and 15 Meters with Visible shape image |
| 6 | video Format | H.264 |
| 7 | FPS | 1080P 30 FPS |
| 8 | White Balance | Yes |
| 9 | Photo Resolution | 8640*4752 |
| 10 | Recording Resolution | 1920*1080 |
| 11 | Storage Capacity | 16GB/32GB/64GB/128GB |
| 12 | Dimension | 86*62*34mm |
| 13 | Weight | 165g |
| 14 | Battery Capacity | 2 pcs Replaceable battery, 1950mAh each |
| 15 | Continuous Running Time | ≥6h with one battery |
| 16 | Secondary Light Source | Infrared Light, LED flash, Laser |
| 17 | Audio Record | Yes |
| 18 | Working Temperature | -40--60℃ |
| 19 | Working humidity | 40%-80% |
| 20 | Storage Temperature | -20--55℃ |
| 21 | Log | Yes |
| 22 | GPS | Built in GPS |
| 23 | Charging Stand | Yes |

Packing List

| No. | Item | Number |
| --- | --- | --- |
| 1 | Body Camera & Clamp | 1 unit |
| 2 | Battery | 2 units |
| 3 | Charging stand | 1 unit |
| 4 | USB cable | 1 set |
| 5 | Adapter | 1 set |
| 7 | Manual | 1 set |
| 8 | Disc | 1 set |